## Slide 1
FINAL REPRODUCIBLE ENGINEERING RELEASE
OpenWing-UAV
A complete CAD · CAM · Aero · FEA · Optimisation · Prototype-validation digital thread for a modular UAV wing.
GitHub-ready v1.0 release framework
Home-PC feasible engineering workflow
Release gate: every claim links to evidence
Author: Samuelson G
OpenWing-UAV v1.0 · Samuelson G
01

## Slide 2
The portfolio challenge
Show credible aerospace CAD/CAM/CAE capability without needing a factory or wind tunnel.
1
Design depth
Parametric wing, aileron, spars, ribs, joiner, hinges and manufacturable parts.
2
Engineering proof
Loads, FEA, buckling, modal response, optimisation and test correlation.
3
Open-source credibility
Repository validation, data schemas, dashboards and release manifests.
Result: a project that demonstrates the full engineering loop, not only a CAD model.
OpenWing-UAV v1.0 · Samuelson G
02

## Slide 3
Digital thread architecture
Every output is linked to a source model, requirement, dataset or test.
CAD
Parametric wing
CAM
CNC + AM
Aero
OpenVSP/XFOIL
FEA
Static + modal
Optimise
Pareto trades
Prototype
Proof + modal
Correlate
Model update
Release
Manifest + site
Core rule
No result is “final” unless its source data, units, coordinate system, revision, acceptance criterion and limitation are recorded.
OpenWing-UAV v1.0 · Samuelson G
03

## Slide 4
Baseline wing specification
A compact UAV half-wing that is still rich enough for real engineering validation.
1.200 m
span
0.240 m²
area
NACA 4412
airfoil
3°
dihedral
−2°
tip washout
64.356 N
+ ultimate half-wing
27.581 N
− ultimate half-wing
6.0
aspect ratio
OpenWing-UAV v1.0 · Samuelson G
04

## Slide 5
Validation stack
The model becomes credible only when analysis and experiment agree within defined targets.
Aero loads
OpenVSP, VSPAERO, XFOIL, parasite drag, stall sensitivity
Structural FEA
Static, contact, adhesive, modal, buckling, fatigue, nonlinear
Prototype tests
Coupons, spar, root joiner, aileron, proof, ultimate, modal
Correlation
Model updating, evidence matrix, independent validation case
Acceptance examples: reaction equilibrium ≤1%, displacement correlation ≤10%, first bending frequency error ≤5%, torsion ≤7%.
OpenWing-UAV v1.0 · Samuelson G
05

## Slide 6
Repository automation
The project is packaged as a reviewable, reproducible GitHub repository.
CSV schemas
Required columns for controlled evidence tables
Validation CI
Checks paths, config, CSV headers, Pages files and temp files
Dashboard data
Generates a JSON catalogue for the portfolio site
Release manifest
Creates SHA-256 hashes for every release artefact
Release gate
Blocks final claims until required evidence is complete
Validated package: 71 repository files · engineering templates · GitHub Pages site · release framework
OpenWing-UAV v1.0 · Samuelson G
06

## Slide 7
v1.0 evidence gate
The final release separates “framework ready” from “engineering validated.”
Ready now
Repository scaffold, website, validators, manifests, v1.0 checklists, release notes, presentation assets.
Requires evidence
CAD baseline, solver outputs, coupon data, proof tests, modal results and correlated FEA model.
Final claim
Only after every required matrix item points to reviewed evidence with traceable revision and units.
Honest release status is a feature: it shows discipline, not weakness.
OpenWing-UAV v1.0 · Samuelson G
07

## Slide 8
Skills demonstrated
A single project covering the complete aerospace engineering workflow.
CAD
SolidWorks part, multibody, assembly, drawings
CAM
DXF, CNC routing, joiner machining, setup sheets
AM
STL/3MF, print orientation, fit coupons
Aero
OpenVSP/VSPAERO, XFOIL, performance envelope
FEA
Static, contact, buckling, modal, fatigue, nonlinear
Testing
Coupons, proof loads, modal hammer, correlation
Optimisation
Design studies, Pareto ranking, uncertainty
DevOps
GitHub Actions, Pages, manifests, schemas
Portfolio takeaway: design thinking + simulation literacy + manufacturing realism + open-source discipline.
OpenWing-UAV v1.0 · Samuelson G
08

## Slide 9
Path beyond v1.0
The repository is ready to become a real test-correlated engineering baseline.
v1.0
Populate evidence and tag reproducible release
v2.0
Integrate fuselage, empennage, propulsion and complete-aircraft stability
v3.0
Add flight-test data, telemetry processing and validated operating envelope
Next action: upload the repository, replace OWNER placeholders, enable Pages, and begin filling the release evidence matrix.
OpenWing-UAV v1.0 · Samuelson G
09